IPVGate20A and “PROTEI – m.Access” for NGN applications.

| mAccess is a line of Next Generation equipment for providing access to modern IP-network communications services. With support for a vast array of network technologies, mAccess can work both in NG and traditional telephone networks. This enables network operators to make the transition to NGN with minimal expense and disruption, allowing them to escape from the limited range of services available in traditional networks and offer their users the full Triple Play services package. The hardware platform is exceptionally scalable and makes it feasible to provide NGN services in any size of installation, from just a few users up to any thousands. mAccess solutions can work with softswitch or equivalent equipment from a hird-party supplier, making them ideal to use for expanding or modernizing existing networks. Regular compatibility testing ensures reliable operation with existing as well as newly-released NGN equipment. The software protocol modules used in mAccess equipment are also kept updated to guarantee dependable performance. The mAccess line covers equipment for use in urban, rural and corporate networks where both traditional and NG services are required. |
| --- |
| IPVgate-20A is a cost-effective, cutting-edge, standalone analog VoIP gateway, fully interoperable with leading soft switches and SIP servers. Note: IPVgate-20A is part of the RAD VoIP System (RVS) product line. The device employs superior voice technology for connecting legacy telephones, fax machines and PBX systems to IP-based telephony networks, as well as for integrating into new IP-based PBX architecture. IPVgate-20A is an intelligent communications center designed to handle all office or home connectivity needs. With its superior QoS mechanism, IPVgate-20A presents a business class solution for today's emerging broadband access services. IPVgate-20A handles telephony, Internet, security networking (internal network LAN and WAN), communications and access to both telephony services and data using an integrated ADSL2+ modem, Ethernet WAN port or fiber optic interface (SFP interface). IPVgate-20A provides full telephone line replacement to allow fast and reliable transition of the customer's Telecom lines into the next generation VoIP-based solutions. VOIP SIP SUPPORT IPVgate-20A enables connecting to any other SIP device by just dialing its number. Fax machines connected to IPVgate-20A benefit from high quality T.38 support, which assures effective and reliable fax transmissions. IPVgate-20A generates call quality information to the RADview management station to track and analyze the QoS. VPN Branch offices can be easily and securely connected to the HQ using the built-in VPN IPSec server/client. Utilizing a 3DES encryption algorithm and up to 10 tunnels per device, IPVgate-20A creates transparent connectivity of enterprise LANs into a single virtual LAN. Note: IPVgate-20A devices with 2 FXS ports support 2 tunnels. FAILSAFE SUPPORT IPVgate-20A performs SIP fail backup by DNS number resolving. When a central SIP server fails to respond, IPVgate-20A accesses the operator or enterprise DNS server to resolve the IP address of the VoIP trunking gateway or of another end-point device. IPVgate-20A is also available with an ADSL2+ modem, to provide ADSL line monitoring and re-routing all traffic information to a backup router (e.g., ISDN router) upon connectivity failure. VoIP-based PSTN Access for SME and/or SOHO Customers WIFI INTERFACE The optional WiFi interface uses an internal WiFi adapter with dual antennas. The WiFi adapter is compatible with IEEE 802.11g, which provides wireless Ethernet access at rates up to 54 Mbps, and with IEEE 802.11b, which provides rates up to 11 Mbps. To achieve maximum reliability, throughput and connectivity, the IEEE 802.11g data rate is automatically and dynamically scalable to 48, 36, 24, 18, 12, 9 and 6 Mbps. The encryption mode is user-selectable: in addition to no encryption, which can be used to build a public access point, IPVgate-20A also supports various wireless data encryption options. | Equipment • mAccess.MAK – a multiservice subscriber access gateway for providing users with Triple Play and traditional voice services. • mAccess.MTU – a multiservice subscriber access gateway specially designed for efficient use in low-capacity applications. MTU-A24 front view: MTU-A48 front view: • mAccess.DMUX - a subscriber gateway that provides users with access to broadband data transfer and telephony services using xDSL technology. Among the exceptional features of the mAccess line are: • Flexibility. The variety of board types vailable simplifies expansion and modernization, and the hardware design allows subscriber boards to be changed without hutting the system down. New revenue-generating services can be added quickly and easily. The architecture used in mAccess allows solutions that combine a range of services in one chassis: connection of analog and IP-terminals, delivery of ADSL2+ and Ethernet connections to subscribers’ premises and the use of Ethenet, SHDSL, VDSL and PCM for connection to the network. • Unified maintenance system. System maintenance can be carried out using a number of means: Telnet/SSH, FTP, a graphical Web interface and command line interface. The system for controlling equipment status and various levels of alarm signal features an SNMP interface and can be integrated with existing monitoring systems already in the network. The complete system makes mAccess maintenance simple and convenient. • Adaptation. mAccess equipment can be installed in existing telecommunications networks and can work using the cable infrastructure resources that are already in place. • Expanded functional capabilities. mAccess line equipment is dual purpose equipment; it can also be used in rugged applications. mAccess.MAK The mAccess line can solve the problem of subscriber base expansion. Subscribers whose terminals are served by mAccess equipment can use traditional telephony services, while if mAccess is used in a multiservice network the full range of Triple Play services becomes vailable. MAccess equipment connects with digital exchanges using a standard V5.2 interface or PRI/E-DSS1 over E1, and connects to multiservice networks using SIP or H.248/MEGACO using various data link-layer technologies. Various types of terminal equipment can be connected to mAccess.MAK, including: • traditional analog telephones; • payphones for local and intercity calls; • fax machines; • modems, etc. The mAccess.MAK multiservice subscriber gateway provides subscribers with access to Triple Play services. Modular construction means the gateway is easily scalable to ncrease subscriber capacity and also allows the creation of combined solutions. mAccess.MAK is built on the following modules: • CONSUL – gateway controller holds main processor, VoIP gateway up to 120 simultaneous calls, TDM-switching matrix and up to 16 E1 trunk ports (optional). Provides interface with exchange. • SLAC30 & SLAC 48 – FXS lines boards for connecting two-wire analogue telephones. SLAC module supports 30 or 48 FXS ports. • SDSLC, VDSLC, ADSLC, ADSLC2 – modules for data transfer using SHDSL, VDSL, ADSL and ADSL2+ accordingly. • ITC – VoIP gateway module for connecting mAccess.MAK to NG networks. Usually ITC module is used when it needs to increase the amount of simultaneous calls passed via m.Access.MAK over 120 calls that support CONSUL module onboard VoIP gateway. Depending on the functions required, mAccess.MAK can be set up with a combination of various modules. As well as providing subscriber access, mAccess.MAK can also provide transfer of voice traffic between NG and traditional telephone networks. mAccess.MAK: • Provides dial-up access to telephone network services. • Delivers voice to multiservice network subscribers. • Delivers of data transfer services using Ethernet and ADSL2+. • Subscriber load multiplexing • Internal switching of voice channels and IP packets. • Flexible scaling and configuration. • Simple to use and maintain. • Wide range of connection interfaces. |
| Specifications NETWORK INTERFACE WAN Ethernet 10/100BaseT ADSL2+ Annex A ADSL2+ Annex B (ADSL over ISDN) SFP slot for fiber interfaces (up to 100 Mbps) Note: For detailed information on SFP interface modules, refer to the SFP Transceivers datasheet. LAN Four Ethernet ports 10/100BaseT auto-sensing auto-crossover switch Connectors Ethernet: RJ-45 ADSL: RJ-45/RJ-11 ADSL2+ MODEM Supports Multimode Standard ADSL2 ITU G.992.3 Annex A (G.dmt.bis), ITU G.992.4 Annex A (G.lite.bis) ADSL2+ ITU G.992.5 Annex A Supporting up to 8 PVCs F4/F5 OAM Supports VC-based and LLC-based multiplexing DATA TRANSFER PROTOCOLS IPv4 Router with NAT/NAPT RIP II DHCP client/server SNTP DMZ PPPoE/PPTP PPPoA, IPoATM (ADSL version) SECURITY SSLv3 Encrypted Phone/Fax P2P VoIP calls VPN IPSec server/client with tunnel IP-filtering Number of tunnels: 4 FXS – supports up to 10 tunnels 2 FXS – supports up to 2 tunnels Firewall Stateful Packet Inspection (SPI) TELEPHONY Number of Lines 2 or 4 analog FXS Connectors RJ-11 Features Call waiting Call progress tones per country DTMF detection Extension-to-extension call | mAccess.MTU mAccess.MTU is a low-capacity multiservice subscriber access gateway built on IP technology. mAccess.MTU allows 8, 16 or 24 analog user terminals to be connected. mAccess.MTU is based on access technologies which allow the operator to provide subscribers with a full range of modern services, helping solve the problem of providing telecommunications services to small-scale end points. mAccess.MTU enables the transfer of voice and fax information over networks with IP packet routing using RTP protocol with SIP and H.248/MEGACO signalling. mAccess.MTU can be connected to the IP network via an SHDSL interface with data transfer rates of up to 8 Mbit/s, or via a VDSL interface. This makes it possible to provide subscribers with high-speed internet access, even using the existing copper-wire telephone line infrastructure. ADSL2+ enables operators to expand their range of services considerably, including services requiring high data transfer speeds - up to a maximum of 24 Mbit/s downstream and 2 Mbit/s upstream. These features make mAccess.MTU ideal for installation in urban, rural and corporate networks. In all cases the equipment allows provision of traditional telephony services, Triple Play and high speed Internet access. mAccess.MTU allows analog user terminals to be connected to the external network using an Ethernet interface (Ax/Eth modification) or xDSL (Ax/DSL modification). If the subscriber uses a PBX, it can also be connected to the external IP network through mAccess.MTU, but through a PRI interface and then over Ethernet (E1/Eth modification) or xDSL (E1/DSL modification). mAcess.MTU can be used in a wide variety of situations. In urban networks, mAccess.MTU can serve as an subscriber’s gateway for providing private subscribers with modern services. The scalability of mAccess.MTU-based solutions makes the system ideal for modernizing urban networks of various types and capacity. Using high-capacity equipment in rural networks with a low subscriber concentration is not always an appropriate solution. mAccess.MTU can be used to bring modern services and multiservice network features to low-population areas. With Access.MTU in a corporate network, the company using the system does not need to install a PBX. Network users can access traditional telephony services, a wide range of additional services and data transfer. mAccess.MTU assumes the simultaneous connection of analog terminals and IP telephones, significantly increasing the number of possible approaches to building corporate networks. The inbuilt Ethernet interface allows mAccess.MTU to |
| Extension-to-VoIP call Call hold Call transfer Music on hold Line grouping Ring Voltage 90 VDC Caller ID Type II CLIR CLIP VOICE OVER IP SIPv2 based UDP/RTP packets Silence suppression Echo cancellation VAD CNG Dynamic jitter buffer Modem pass-through Fax T.38 compliant Group-3 fax relay Fax bypass Compression G.711 G.723.1 G.729A QoS Diffserv Upstream priority WIFI INTERFACE Compliance As per IEEE 802.11g As per IEEE 802.11b Operating Band 2.4 GHz, channels 1 to 11 Antennas Two 5 dBi antennas, polarity adjustable in ±90 degree range around vertical Transmission Rate Up to 54 Mbps, with automatic dynamic scaling to 48, 36, 24, 18, 12, 9 or 6 Mbps (IEEE 802.11g) Up to 11 Mbps (IEEE 802.11b) Security Support Wired Equivalent Privacy (WEP) WiFi Protected Access (WPA) WiFi Protected Access 2 (WPA2) WPA + WPA2 modes MANAGEMENT Quick-install web page Remote ADSL line quality monitoring RS-232 port for basic configuration Telnet FTP server Remote update/upgrade | be connected to a LAN switch, providing high-speed corporate Internet access. The Ethernet interface provides 100 Mbit/s. The system features all the necessary interfaces for connection with the subscriber softswitch mCore.MKD-5 and third-party solutions. mAccess.MTU is also suited to delivering Triple Play services to subscribers. Application Using mAccess.MAK in circuit-switched networks. mAccessMAK connects to the digital exchange by E1 using standard interfaces V5.2 (with multiplexing) or PRI/E-DSS1 to provide subscribers with PSTN services. mAccess.MAK connects to the exchange using from 1 to 16 standard E1 interfaces. This provides: • establishment of incoming and outgoing connections (local, intercity and international calls); • delivery of additional services to subscribers with analog terminal equipment using facilities available on the branch exchange (only when V5.x multiplexer is connected) or PBX; • transmission of tarrification signals for payphones; • provision of telephony, 3.1 kHz, unlimited 64 kB/s data transfer; • fax and modem session support. Using mAccess.MAK in NG networks. The MAK gateway can transfer voice traffic and fax information over networks with IP packet routing. mAccess.MAK supports SIP and H.248/MEGACO protocols to interact with softswitches in multiservice networks VLAN greatly simplifies the task of working with different data types while maintaining quality of service. The use of ADSL2+ allows the operator to transmit data at rates of up to 24 Mbit/s downstream and 2 Mbit/s upstream. With mAcess.MAK, the ease of expanding subscriber capacity and the capacity for combined solutions help the operator to build networks with minimal expenditure, raise turnover and increase profits. mCase enclosures and cabinets are used for mAccess.MAK outdoor installation: • mCase1000 • mCase500 • mCase200 Cabinets are required for protecting equipment from the outside environment and from unauthorized access. The street enclosure is equipped with climate control, power supply and |
| GENERAL Physical Height: 4.85 cm (1.9 in) Width: 21.8 cm (8.6 in) Depth: 19.1 cm (7.5 in) Weight: 0.875 kg (1.9 lb) Environment Operating Temperature: 5° to 40°C (41° to 104°F) Storage Temperature: -25° to 70°C (-77° to 158°F) Humidity: Up to 90%, non-condensing | signalling sensor equipment. The climate control system protects equipment from overheating and from excessively low temperatures. Street enclosures have heating and thermally insulated walls and doors. The subscriber and exchange connection junctions are housed in separate sections to minimize the risk of harm from environmental conditions (rain, snow, low temperature) during maintenance when the enclosure doors are open. This additionally reduces the risk of unauthorized access and vandalism. mCase enclosures feature a door sensor (detects when doors are opened), temperature sensor and a fire safety sensor. |
|  | Basic mAccess specifications mAccess.MAK Number of analog two-wire interfaces: • 6U 19” chassis – up to 912 FXS lines Interface boards: • analogue two-wire FXS board – 30 or 48 ports • ADSL2+/ADSL board -24 ADSL + 24 POTS (FXS) ports Transport boards: • SHDSL board - 8 SHDSL interfaces • VDSL board - 8 VDSL interfaces VoIP codecs - G.711, G.723. G.726, G.729. Exchange interface - E1 (2048 Kbit/s, G.703, 120 Ohm, HDB3) Subscriber interfaces - FXS, ADSL2+, PRI, 10/100 Base-T Connection protocols: • to TDM exchange - V5, PRI/EDSS1, 2ВСК, ISUP-R • to multiservice network nodes - SIP , H.248/MEGACO Services – VAS, PSTN, NGN Maintenance - Secure Web control, CLI, telnet/SSH, FTP, SNMP Chassis dimensions: - Width - 482 mm / 19 inches - Height – 6U (246 mm) - Depth – 300 mm - Weight – approx 15 kg (with typical boards set) Powering - -48V (-10/+15%) -60V (-10/+15%) Power consumption Per one analogue interface - No greater than 0.4 W |
|  | Basic mAccess specifications mAccess.MTU Number of analogue two-wire FXS interfaces: • 1U 19” module – 8/16/24/48 Supported signalling protocols: To the network - SIP & H.248/MEGACO To the user side – EDSS1, FXS VoIP codecs - G.711, G.723. G.726, G.729. Interface types: – Ethernet 100 Base-T – SHDSL – ADSL2+ – VDSL - analog FXS - PRI Maintenance - Secure Web control, CLI, telnet/SSH, FTP, SNMP Povering - 220/12V adapter in subscriber premises |