“IPVSuite – 200” and “PROTEI – mCore” for NGN solutions.

| In NGN networks, call and service control is separated from transport functions. As a result, it is now possible to use single service logic regardless of the carrier and exchange technology. Call control in NGN networks is handled by the softswitch. The softswitch is the central element of NGN, thus the quality and reliability of the network depend heavily on the correct choice of softswitch. The PROTEI mCore solutions line is a combination of softswitches of various classes. Installing mCore in an existing telephone network makes it possible to deploy an NGN segment and connect to other elements of the network through gateway equipment. mCore can be deployed in metropolitan as well as rural settings. It can also be used for creating office and corporate networks. mCore - bsaed networks support new Triple Play and IN services along with traditional telephone network services. |
| --- |
| IPVSuite-200 | mCoer |
| IPVsuite-200 is a carrier-grade softswitch solution using the SIP protocol that enables carriers and newcomers to integrate voice data and multimedia services on a comprehensive packet switching platform, providing extensive Class 5 (and partial Class 4) traditional and next generation services. IPVsuite-200 is part of RAD VoIP System (RVS) product line that includes CPEs (IPVgate family), prepaid/postpaid billing (IPVsuite-Billing) and additional complementary elements. IPVSUITE SOFTSWITCH IPVsuite-200 provides standard CDR (Call Data Records) to billing systems and stores its data and configuration data in a robust Oracle database. VoIP SIP SUPPORT IPVsuite-200 enables connecting any standard SIP client after its authentication and registration. Connected SIP clients benefit from Class 5 services provided and managed by the IPVsuite Softswitch. FAILSAFE SUPPORT IPVsuite-200 can be deployed in a distributed switch architecture to ensure system redundancy and carrier-class availability of service. MANAGEMENT AND MONITORING SYSTEM IPVsuite-200 includes the IPVsuite centralized service management platform. The IPVsuite includes one or several clusters, which consist of a communications server and a database (Oracle) server, to provide remote management, real-time monitoring statistics, network analysis, secured registration and other advanced services. This comprehensive provisioning system enables providers to view, manage, maintain and configure various CPEs and applications installed in the network, thus reducing integration and operational costs of the CPEs (Customer Premises Equipment) network. IPVsuite-200 provides key provisioning services such as security, address resolution, real-time monitoring, service activation, analysis and error management. It also generates usage and CDR information and provides massive remote upgrading capabilities. Specifications SERVERS Basic Configuration: 2 servers (front end and back end) Redundant Configuration: 4 servers with high-availability cluster architecture RAID diskOracle™ database Linux perating System PROTOCOLS HTTP/HTTPS server FTP server D-DNS server IP-TELEPHONY SIP-based Softswitch (stateful) supporting 400,000 BHCA and above Call routing plans: Static Based on type of call (e.g., fax, modem) Based on caller/called Based on day and time Personal end-user web pages: Call-log pages Service activation and configuration Line grouping MSN (Multiple Subscriber Numbers) DDI/DID (Direct Dial-In/Direct Inward Dialing) Compliant to leading VoIP media gateways Compliant to SIP end-units: Soft-phones (e.g., Microsoft Messenger) IP phones IP-PBX Figure 2. | The mCore solutions line is as follows: • mCore.MKD-4 – Transit softswitch; • mCore.MKD-5 – Softswitch for building subscriber networks; • mCore.CPBX – IP-PBX, Centrex PBX equipment. mCore.MKD-4 – a transit softswitch with functions for load balancing according to destination, collection of statistics and storage of detailed information about connections. Suitable for varied applications involving routing of user information streams. mCore.MKD-5 – class 5 softswitch that operates as a control node in NGN. mCore.CPBX – a device specially developed for building corporate networks. Features a wide range of functions for use in administrative networks. mCore.MKD equipment is designed for call routing, controlling access equipment and providing intellectual services in NG networks. Ordinary HP (DL160, DL360 etc) or IBM servers running under Linux Operating System could be used as hardware base of softswich on mCore software. Call processing server and Operating Management Server SW are running on the same hardvare. In case redundancy required, most important elements like CPS, EPS and internal LAN are doubled: mCore specifications Number of subscribers served in standard configuration: mCore.MKD-4, mCore.MKD-5 - Up to 25000 subscribers mCore.CPBX - Up to 5000 subscribers Protocols for connection to NGN nodes: SIP, SIP-T, SIGTRAN, H.248 Protocols for working with billing systems and AAA systems: RADIUS, CDR sending Supported additional services: - Autoredial (CCNR) - Call interception (LH) - Call holding (HOLD) - Invitation to conference (CONF) - Call transfer (CT) - Various types of redirection (CF) - Subscriber-group connection (CUG) - Call waiting (CW) - Hotline - Centrex services - Intelligent Network services (IN) - ‘Private office’ services - Voice instructions, welcome messages and others *Flexible options for creating new services Maintenance: Secure WEB management of configuration, CLI, Telnet/SSH, FTP, SNMP Power supply: 1) -48В (-10/+15%) DC -60В (-10/+15%) DC 2) - 220B AC In metropolitan, rural and corporate networks, mCore also routes calls, provides a range of additional services and manages connection establishment and associated processes. mCore is the central part of PROTEI Lab. NGN solution that include in addition VoIP subscribers access multiplexers up to 912FXS lines per shelf (m.Access family) and VoIP gateways up to 80 E1 trunks TDM networks connection per shelf (mGate family). Such parts of the PROTEI Lab. NGN solution like IP-based Call center, Interactive voice response (IVR), prepaid cards processing & billing platform could be implemented separately as independent products. Functionality of mCore based softswich mCore.MKD connects to the carrier IP network through an Ethernet 100/1000 Mbit/s interface using SIP, H.248/MEGACO signaling protocols. SS7 and EDSS-1 are transferred over the SIGTRAN protocol via a gateway to existing PSTN networks. mCore can provide connection between different networks and can be used to set up connection between IP and PSTN networks. SIGTRAN protocol via a gateway to existing PSTN networks. mCore can provide connection between different networks and can be used to set up connection between IP and PSTN networks. mCore system provides a wide array of functions, including: • Call routing. A specially developed PCP system is used for configuring call routing in mCore.MKD. The choice of node used for call servicing is made on the basis of the source and destination numbers, the source IP address, destination and a number of other call parameters. • Provision of Additional Services. mCore can provide users with a wide range of additional Centrex and various special services, such as ‘private office’. mCore controls user privileges for access to additional services. • Provision of Intelligent Services. The mCore line of solutions is fully compatible with the PROTEI Intelligent Services platform, which provides a wide range of services including call centers, voice mail, IVR, calling cards and much more. • Basic call service. mCore equipment provides basic voice call services and allows flexible call routing rules. • CDR and statistics. mCore.MKD records data related to calls and services handled by the system. CDR information is stored for every attempted (successful or not) call. These records can be used by the billing system for calculating call costs as well as for amassing statistics. • Lawful Intercept Functions. Intended for sanctioned interception of calls made by subscribers under the surveillance of lawenforcement bodies. • Session Border Controller (SBC) applications. |
| IVR Options Fully integrated with RAD’s IPVsuite-200 Class 5 SIP softswitch and provisioning system, the IPVsuite-Billing prepaid server includes service applications for zero-stage direct dialing services without IVR, single-stage dialing services with IVR (for registered prepaid subscribers) and dual-stage dialing services with IVR (for prepaid calling cards). User-friendly Web Interface The IPVsuite-Billing Web interfaces provide up-to-the-minute account information for both the subscribers and customer service representatives (CSRs). Using the WebClient application, CSRs can easily create, search and modify Accounts, view account activities, balances and invoices, and manage support ticklers. Customers are able to manage their own accounts, register to new services, and make payments online through Web-based self-care interface. Calling card customers can change their PIN numbers and top-up their balance via the Web or over the phone using an IVR system. | Capabilities Construction of metropolitan telephone networks. Installing mCore.MKD-5 equipment in the central exchange creates the option to serve subscribers connected to it with a wide range of additional services and a new level of service quality. Full compatibility with PABXs allows a gradual changeover of equipment when modernizing the network. mCore in combination with mAccess and mGate allows the construction of NG networks of any scale and for any purpose. Construction of rural telephone networks. mCore in combination with mAccess and mGate give significant advantages when building rural networks in areas with low terminal concentration and uneven distribution of users. mCore is installed as a central station. The PROTEI mAccess line (mAccess.MTU, mAccess.MAK) can be used for branch stations. Using mCore gives rural subscribers access to the entire range of services provided by IN and NGN. Construction of corporate networks. The best solution for building corporate networks is to use mCore.CPBX. The expediency of this solution is easily justified – with minimal outlay, it provides access to the full range of next-generation services. It allows connection of analogue terminals as well as IP telephones and PCs with appropriate software. Construction of transit networks. Both our own gateway and third-party equipment can be used when employing mCore equipment for providing inter-network transit between operators. The transit network can be used for connecting networks of different types and, thanks to mCore, it can satisfy the most demanding operator’s needs for running statistics, detailed service records, flexible routing rules and solid reliability. |
| MANAGEMENT AND MONITORING SYSTEM IPVsuite-200 includes the IPVsuite centralized service management platform. The IPVsuite includes one or several clusters, which consist of a communications server and a database (Oracle) server, to provide remote management, real-time monitoring statistics, network analysis, secured registration and other advanced services. This comprehensive provisioning system enables providers to view, manage, maintain and configure various CPEs and applications installed in the network, thus reducing integration and operational costs of the CPEs (Customer Premises Equipment) network. IPVsuite-200 provides key provisioning services such as security, address resolution, real-time monitoring, service activation, analysis and error management. It also generates usage and CDR information and provides massive remote upgrading capabilities. RESELLER SEGMENTATION The owner of the IPVsuite-200 (the main provider), can break this system down into segments. These segments or virtual subsystems are run by sub-providers - operators or resellers. This kind of segmentation allows the sub-providers to run their own VoIP service networks over the existing platform with zero cost of ownership. Each sub-provider can create, monitor and manage his own subscribers, while the main provider maintains control over the subscribers of all the sub-providers. | mCore equipment line features • Support for large number of signaling protocols. mCore supports SIP, H.248/MEGACO for connection to IP network elements and SIGTRAN for transfer of SS7 or EDSS-1 signal information. • Modular architecture. This approach to system architecture allows functional duties to be divided among different modules, allowing for ease of use and maintenance and making it possible to create high performance cluster solutions. • Audio signal generation. The mCore.MKD switch can generate various sound signals such as ‘ringing’, ‘engaged’ and others, as well as playing voice instructions. Audio signals can be changed by the operator. • RTP proxy capability. mCore can work in one of two RTP processing modes: with or without RTP-proxy. • ‘Alarm signal’. The alarm signaling system allows real-time alert to emergency situations with both mCore and equipment connected to it. Equipment reliability. Redundancy of main mCore elements ensures high reliability. Redundant elements periodically refresh their information from active components. In case of malfunction of a main component, the redundant element takes over. • Remote maintenance capability. mCore system maintenance can be carried out using Telnet/SSH and FTP with a WEB interface and command line interface. Billing System interconnection could be provided via CDR files or RADIUS protocol directly from the m.Core softswitch or via dedicated gateway mGate.CDR/ITG. The last one solution could be used for regions with poor IP infrastructure, where more profitable to place several softswitches in on neighbor territories or towns and make only one PSTN interconnection point for long distant calls. |
| CLASS 5 – TELEPHONY SERVICES of IPVSuite Enhanced Voice Mail: Personalization messages Message forwarding Voice-mail to Email forwarding Auto-Attendant Call forwarding: ETSI dialing support activation Web activation Forward on Busy Forward on No-Answer Forward on Not available Scheduled forwarding DND (Do not disturb) ACR (Anonymous call rejection) Incoming/outgoing call screening Incoming/outgoing call lock Home assistance (emergency dial when off-hook) Last call return Busy call retry 1-800 toll free numbers MANAGEMENT CDR information aggregation Usage audit log (of configurations) Reports and statistics | Basic set telephony services mCore based softswitch: ● basic call; ● entry, replacement or removal of the personal identification code - password; ● ban outgoing calls; ● accompanying call by a password; ● temporary ban on incoming calls (Do Not Disturb); ● cancellation of all services; ● Notification of new incoming calls; ● call forwarding unconditional; ● Call Forward No Answer on the subscriber; ● Call Forwarding employment subscriber; ● direct challenge; ● Call Waiting; ● Call Transfer; ● Confer; ● 3-way conference; ● malicious call identification; ● playing their own numbers; ● abbreviated dialing; ● music on hold. ● Automatic redial if non-response; ● waiting callback; ● prohibition identification number of the caller; ● entry / withdrawal rates in the black list; ● muxing phone number; ● Call Forwarding during the Recall; ● Call Pickup (hunt and pickup group); ● chat room; ● HotDial / FDCI; ● temporary ban on incoming diverted; ● Unified Communication (speech, video, messaging, presence, audio- and video conferencing via softphone). Additional service module mCore based PBX (Virtual PBX module): ● individual musical accompaniment on the expectation for each vPBX; ● Individual IVR for each vPBX; ● Closed Numbering Plan; ● Self-Provisioning. VoiceMail, IVR, Telephony cards processing platform are indepent NGN products of PROTEI Lab and could be described seporately. |